Economics of the Internet

- EE/W1 (No.2E)

  - Outline

- Definitions

collection of digital networks

computers interconnected by communications media

- Technical terms

Ｎ　　　　　Ｎ

Ｎ

Ｎ

The Internet

Upper-case ( a pronoun)

- Internet viewed from a user

  - Access terminals

computers

mobile handset, TV, game terminal

connected to the Internet via communications media

  - ISP（Internet service providers）

access service for the Internet (with fees)

  - LAN（local area network）

network used in offices and schools

cost paid by an organization

Internet use in campus is “free to students”

  - Internet services

    - E-mail

    - web（www）

documents (charactors), images, voice and music,

video images, smell (?) --- anything expressed in digital data

- Structure of the Internet

  - How does the Internet work?

- Outline

a. Internet is a collection of computers.

address attached to each computer

IP address

unique globally

terminals (for users)

servers (for mail, web. etc.)

routers (for data transmission)

b. How is a message sent over the internet?

１．A user submits a message to the nearest server.

２．The message is sent from the server to a nearby router, which sends it to another router, and so on, so that the message will be delivered finally to a destination.

New use with packets：shared use (like streets, highways in transportation)

Old use(exclusive)　　　cost ＝1,000　　　　no congestion

Packet use (shared)      cost ＝1            delay if congested

↓

more efficient

(example) telephone ：　conventional telephone： US-JAPAN　\400／3 min

IP-phone：US-JAPAN　\8／3 min.

- Division of labor in the Internet

- (1)  Division of labor is established in the Internet so as to perform each task efficiently.

- (2)  Consequently, the cost of using Internet services is decreased significantly.

  - The IP platform – the global engine for information transmission

- Characteristics of information transmission over the Internet

- a. Outline

- A system of routers (computers) interconnected in order to transmit and exchange IP-packets.

b. Characteristics

simple and easy task to each counter

a large-scale complicated task achieved by the system as a whole

c. Sources of the efficiency

- Concentration and specialization

Routers concentrate on sending and receiving IP-packet data only.

IP-packets may be transmitted over any media.

IP-packets may carry any content.

- Operations

Internet is composed of many networks.

IP-format and IP-addressing are the only rule to be observed.

Otherwise, member networks may operate freely except that the connection cost should be borne by a new-member network.

(the issue of the cost of cross-pacific connections)

- IP-address

An address of a “number” of 32-bits (0 and 1’s) given to a computer. Every router, server, and user PC connected to the Internet must have a unique IP-address.

- IP-packets

the standard in the internet

IP： Internet Protocol

example: a piece of music may be transformed into a few number of

IP-packets

内容

- Routers

Each router is interconnected to a number of routers.  When a router A receives a packet from an interconnected router B, the router B transmits the packet to another interconnected router C which is located near to the destination of the packet.

  - Internet Applications --- Mail and Web Systems

1. Domain-name system

- Outline

domain name: an address for mail and web services

taro：user name

osaka-gu.ac.jp：domain name

taro@osaka-gu.ac.jp：mail address

”at mark”

domain name： human friendly

（IP-address: OK to routers, not to human beings）

- Domain-name servers (DNS)

(1) Outline

Each network of the Internet should have a DNS.

abc@def.eg.jp ――― an address for sending a mail

What is the IP-address of a computer with the given domain name?

  - (2) Inquiry to DNS

(3) Assignment of domain names

- 2.  Mail system

- a. Outline

The first application of the Internet.

Mail texts are sent in IP-packets to a destination specified by a domain name.

b.  Mail addresses

mail address = user name @ domain name

Ex.：taro@uts.osaka-gu.ac.jp

user name       domain name

(individual)      (students) (academic) (japan)

2. Web System

- Outline

The second major application of the Internet.  On receiving a request from a web user, the web server sends a copy of the requested file (web pages, characters, graphs, tables, musics, or video images) by putting it into one or more IP-packets.  The user, receiving the file, reconstructs the original content on a terminal computer by means of a browser software (such as Intenet Explore).

Web system

A method for obtaining a file stored in a distant computer

web as a network image

Anybody can get a distant file at hand with a single mouse click.  　 The system gives an impression that the user, not a file, is moving around.

# Text boxes

旧来のネットワーク（　 回線方式 　）

ユーザＡ

ユーザＡ

古い使い方

回線は

すきまだらけ

回線を使う（予約）

専用レーン（方式）

0101……………………………………………………………………………………………………

………………...................................................

……………………………………………………

……………………………………………………

……………………………………………………

０と１の並び

（デジタル・データ）

１パケット分

終

宛先

1/3

発信

始

長さ

ヘッダー

ＩＰアドレス（例：133.52.271.01）

フッター

送

パケット

途中で

失われてもそれまで

ISP

ISP

ルータ

ルータ

ルータ

ルータ

ルータ

ルータ

サーバ

ユーザPC

（TCP/IPソフト）

サーバ

「インターネット」

IP=1.11

IP=2.2

IP=1.11

IP=1.1

IP=4.1

IP=3.2

IP=3.21

IP=3.211

IP=1.112

図　ルータ群とIPアドレス（宛先指定）による簡単なIPパケット転送網（ルータ間のバケツリレー型転送）の例

ユーザPC

（TCP/IPソフト）

academic

DNS

osa-gu

DNS

DNS

jp

ドメインの重層構造

アメリカ

世界のどのユーザのメールアドレスでも、ＩＰアドレスに翻訳できる

ac  DNS

us  DNS

jp  DNS

世界DNS

osa-gu DNS

（多数）

（TCPデータ）

I

ルータ

ルータ

ルータ

ルータ

メール送信サーバ（SMTP）

メール受信サーバ（POP3）

メールユーザ

メールユーザ

ドメイン名サーバ

（IPパケット）

I

（TCPデータ）

I

（ISP）

（ISP）

図　メール・サーバによるメール送信

（ファイル請求）

（多数）

ルータ

ルータ

ルータ

ルータ

Proxy

(代理)

サーバ

Webサーバ

（Web用

ソフト）

ユーザPC

（ブラウザ・

ソフト）

（ISP）

（Webサイト）

PC（ブラウザ付）によるWebコンテンツの閲覧システム

サーバ

Web供給者PC

（コンテンツ作成ソフト）

（ファイル登録）

Ip-address (e.g., 133.52.271.01）

header

Lnth

Beg

Orig

1/3

Dest

Endnd

a packet

sequence of 0 and 1’s

0101……………………………………………………………………………………………………

………………...................................................

……………………………………………………

……………………………………………………

……………………………………………………

user PC

（TCP/IP software）

Figure. A simple IP-network

IP=1.112

IP=3.211

IP=3.21

IP=3.2

IP=4.1

IP=1.1

IP=1.11

IP=2.2

IP=1.11

The Internet

データ

server

user PC

（TCP/IP software）

server

router

router

router

router

router

router

ISP

ISP

a line is reserved

exclusive use

Old use of communication lines

User B

UserＡ

Internet

mobile user

server

PC

user

server

footer

a packet

Data

academic

DNS

osa-gu

DNS

DNS

jp

U.S.A.

ac  DNS

us  DNS

jp  DNS

world DNS

Figure:  Sending a mail with mail servers and routers

（ISP）

（ISP）

（TCP DATA）

I

（IP-packet）

I

DNS

mail user

mail user

mail-receiving (post-office)

server

(POPS, SMTP)

（POPS, SMTP）

mail-sending server（SMTP）

router

router

router

router

（TCP DATA）

I

（many）

ＷＷＷ=World Wide Web

(request）

（many）

router

router

router

router

Proxy

server

Web server

（Web-service

software）

user PC

(browsing software)

（ISP）

（Web site）

Figure: Web-browsing System

server

Web provider

（content creation software）

(storing)